## Slide 1: Long Precision Calculator
Name: Siddharth VIJAY BHAMARE
Roll No. : 06
Watumull institute of electronics engineering and computer technogy

## Slide 2: Features of Binary calculator
Performs arithmetic operations on very large numbers
Performs infix solution according to precedence and takes brackets in consideration.
Performs modulus and exponential operations.
Also performs negative and float point numbers.
Performs comparison operations such greater than, less than, equal and not equal.
Performs logical AND and OR operations.

## Slide 3: Number ADT
Number is an ADT used to store very large numbers.
It is structure consisting of integer variable denoting its sign and number of digits after decimal points.
It also consists of two pointers to node adts which in turn is doubly linked list with intergar variable to store single digit number.
MACROs have been declared as PLUS and MINUS to denote the sign of numbers.

## Slide 4: Operations:
Function used for arithmethic operations
Adjustpoint:
  It makes the number of digits after decimal point equal.
  It adds zeroes to the end of number with less float point digits.
Lengthequal:
  Similar to adjustpoint, it also makes number equal , but here for before decimal points.
  It adds zeroes to start of number to make them equal without changing its value .

## Slide 5: Operations:
Function used for arithmeahic operations
3. zeroequal:
  It checks whether entered number is zero or not.
  It is useful to detect error as “division by zero”.
4. Compare:
  It compares two numbers and returns 1 if first parameter is greater than the second.
  It considers the length of numbers. If length are equal it compares each members starting from leftmost number.

## Slide 6: Operations
Addition operation:
  Inside addition operation based on their signs, appropriate function as subtraction are called.
  During addition operation, node adts are used to access each node of both numbers and add them individually.
  Excessive carry generated is added to previous node by floor division by 10.
  Sum is stored is number answer by insert at begin function.
  Extra nodes at a big numbers are added to answer with taking care of carry generated.

## Slide 7: Operations
2. Subtraction operation:
  Subtraction operation works mainly similar to working of addition operation.
  According to its sign , functions are called.
  Node adts are declared and used to access and perform operation on each digits of numbers.
  In case of borrow, it is subtracted from the node previous to it.

## Slide 8: Operations
3. Multiplication operation
  It works mostly same method as we perform on paper.
  One element of multiplier is multiplied with each digit of multiplicand with taking care of its carry and decimal place.
  If one of number is zero, it directly gives answer zero.
  For other case , using node adts, each elements of smaller numbers is multiplied with digits of other numbers.
  The result is stored in the form of array, so accessing them while calculation becomes easier.
  At last, entries in answer array is stored in number adt.

## Slide 9: Operations
4. Division operator:
  Division operation is based on the process of number of subtraction of divisor from dividend.
  If divisor is zero , it throws division by zero error.
  Dividend is divided by divisor, and is product is subtracted from dividend. This is repeated till the number of after decimal points equal to SCALE or it is perfectly divisible.
  Zeroes are pushed to dividend to get accurate divisions.

## Slide 10: Operations
5. Modulus function:
  It works on basic formula of modulus function.
  It obtained by subtracting floor division of dividend from dividend.
  Similarly as division operator, it also gives division error when divisor is equal to zero.

## Slide 11: Operations
6. Power function
  It works on principle of repeated multiplication or division, based on sign of the exponent.
  If exponent is plus signed, base is multiplied with itself exponent number of times. And stored as answer.
  If exponent is minus signed, reciprocal of its exponential answer is taken.
  Sign of negative base is determined by even or odd nature of the exponent.

## Slide 12: Operations
Comparison operations
  Greater than
  Less than
  Equal to
  Not equal to.

## Slide 13: Operations
Logical operations
  Logical AND operation.
  Logical OR operation

## Slide 14: Thank You